## Slide 1
NITROGEN GENERATORS

## Slide 2
BASICS ABOUT AMBIENT AIR
Chart: 
| Nitrogen | Oxygen | Other
Prodaja | 78 | 21 | 1

## Slide 3
BASICS ABOUT NITROGEN AND OXYGEN
REACTIVE
COLORLESS, ODORLESS AND TASTELESS GAS
REACTS WITH MOST OF THE CHEMICAL ELEMENTS
NECESSARY FOR MOST LIVING ORGANISMS AND FOR METABOLIC PROCESSES
OXYGEN
O2
NITROGEN
N2
INERT
COLORLESS, ODORLESS AND TASTELESS GAS
DOES NOT ENTER IN CHEMICAL REACTIONS
DOES NOT SUPPORT COMBUSTION

## Slide 4
NITROGEN APPLICATIONS
INERTING AND BLANKETING
PURITY: 99 – 99,9 %
WINE
OILS (Olive oil, soybean oil, …)
SOFT DRINKS (Juice, mineral water, …)
DAIRY PRODUCTS
  (Milk, powdered milk, cheese, butter, …)
  SOFT DRINKS (Juice, mineral water, …)
TO REDUCE / PREVENT PRODUCT DEGRADATION FROM MOISTURE AND OXYGEN

## Slide 5
NITROGEN APPLICATIONS
CONTROLLED ATMOSPHERE STORAGE
PURITY: 95 – 99,99 %
FOOD PRODUCTS
FRUITS
VEGETABLES
TO PRESERVE FRESH FRUITS AND VEGETABLES

## Slide 6
NITROGEN APPLICATIONS
MODIFIED ATMOSPHERE PACKAGING (MAP)
PURITY: 95 – 99,5 %
MEAT PRODUCTS
PRE-COOKED FOOD
WINE
DAIRY PRODUCTS
PHARMACEUTICAL PRODUCTS
TO EXTEND SHELF LIFE

## Slide 7
NITROGEN APPLICATIONS
INDUSTRIAL APPLICATIONS
PURITY: 95 – 99,9999 %
LASER CUTTING
ELECTRONICS
GAS INJECTION MOULDING
PROTECTIVE ATMOSPHERE IN EXPLOSIVE AREA
TO ASSURE STABLE QUALITY / TO IMPROVE PROCESS QUALITY / SAFETY

## Slide 8
Application | Purity as % of O2 | Pressure of N2 (barg) | Specific Requirements
Food procesing -MAP - Wine Sparging Control atmosphere Meat packing | 2- 0,5 | Low | Sterile Filtration
Blanketing | 2-5 | Low | 
Gas Injection Molding | 0,5-1 | High | Booster
Electronics | 0,1 – 0,01 | Low | 
Lasser cutting | 0,0001 | 30 or 250 | Booster
APPLICATIONS PROCESS REQUIREMENTS

## Slide 9
MEDIUM-HIGH PURITY (to 99,9999%)
HIGH CAPACITY ( > 10.000M3/H)
HIGH INVESTMENT
LOW PRODUCTION PRICE
NITROGEN PRODUCTION METHODS
MEMBRANE
PRESSURE SWING ADSORPTION PSA
CRYOGENIC PLANT
LOW-MEDIUM PURITY (90 TO 99,5%)
LOW CAPACITY (UP TO 1000M3/H)
LOW INVESTMENT
MEDIUM PRODUCTION PRICE
LOW-HIGH PURITY (90 TO 99,5%)
MEDIUM CAPACITY (< 10.000M3/H)
MEDIUM INVESTMENT
MEDIUM PRODUCTION PRICE

## Slide 10
99,9999
99,999
99,99
99,9
99
90
1
10
100
1000
10000
100000
MEMBRANE
LIQUID NITROGEN
PSA
CRYOGENIC NITROGEN PLANT
CYLINDER
Nitrogen purity [%]
Nitrogen consumption [Nm3/h]
NITROGEN PRODUCTION METHODS

## Slide 11
WHY GENERATE YOUR OWN N2 / O2 RATHER THAN USING LIN?
CONTRACT SUPPLY
PSA GENERATOR

## Slide 12
Safety reason
Simple and Ready on demand
Total control over production
Production capacity fit your needs
No icing of the liquid gas tanks
No losses of the gass due to evaporation
Lower costs
No contractual limitations
WHY GENERATE YOUR OWN GAS RATHER THAN USING CONTRACT SUPPLY?









## Slide 13
HOW PSA GAS GENERATOR WORKS
Adsorption
Regeneration
N2
Compressed air
Pressure building phase
N2
N2
N2
N2
O2
O2
O2
O2
O2
t

## Slide 14
HOW PSA NITROGEN GENERATOR WORKS
N2
Adsorption
Pressure equalization phase
Depressurization
Pressure building phase
Regeneration
t

## Slide 15
ADSORPTION MECHANISM OF CMS

## Slide 16
COMPRESSOR STATION WITH PSA GENERATOR
COMPRESSOR
OIL LUBRICATED / OIL FREE
AIR TREATMENT
Class 1.4.1. acc. To ISO 8573-¸1
AIR BUFFER
TANK
GENERATOR
NITROGEN BUFFER TANK

## Slide 17
BUFFER TANKS
COMPRESSED AIR CONSUMPTION
NITROGEN CONSUMPTION
Consumption
Time
Consumption
Time
Consumption
Time
STEADY
PERIODIC

## Slide 18
N-GEN SERIES NITROGEN GENERATOR
STANDARD EQUIPMENT
• SET OF EXTERNAL FEED AIR FILTERS
• ADSORBER VESSELS
• PNEUMATIC VALVES
• INTERNAL PIPING & FITTINGS
• MAINTENANCE-FREE EXHAUST SILENCERS
• AIR AND NITROGEN PRESSURE REGULATION
• LOCAL INSTRUMENTATION
• CONTROL SYSTEM WITH SIMENS LOGO
• PRESSURE SWITCH FOR AUTOMATED STAND-BY MODE

## Slide 19
N-GEN SERIES NITROGEN GENERATOR
OPTIONAL EQUIPMENT
• OXYGEN ANALYSER WITH ZIRCONIUM-OXIDE SENSOR
• ELECTRONIC PRODUCT FLOW METER
• FEED AIR / PRODUCT MOISTURE ANALYSER
• FEED AIR / PRODUCT TEMPERATURE TRANSMITTERS
• NITROGEN STERILE FILTERS
• NITROGEN BOOSTER
• NITROGEN CYLINDER FILLING SYSTEM
• TOUCH SCREEN DISPLAY

## Slide 20
Model | INLET PRESSURE [barg] | DISCHARGE PRESSURE [barg] | NITROGEN PURITY [vol. %] |  |  |  |  |  | 
 |  |  | 97 | 98 | 99 | 99,5 | 99,9 | 99,99 | 99,999
N GEN 05; N2 flow [Nm3/h] | 7,5 | 6,6 | 9,0 | 7,4 | 6,2 | 5,2 | 3,4 | 1,7 | 1,1
Feed air consumption [Nm3/h] |  |  | 23,2 | 21,0 | 19,7 | 18,0 | 14,5 | 10,5 | 9,5
N GEN 10; N2 flow [Nm3/h] | 7,5 | 6,6 | 15,2 | 12,4 | 10,5 | 8,7 | 5,8 | 2,9 | 1,8
Feed air consumption [Nm3/h] |  |  | 38,9 | 35,3 | 33,0 | 30,2 | 24,3 | 17,6 | 15,9
N GEN 15; N2 flow [Nm3/h] | 7,5 | 6,6 | 24,1 | 19,7 | 16,7 | 13,8 | 9,2 | 4,6 | 2,8
Feed air consumption [Nm3/h] |  |  | 61,8 | 56,1 | 52,5 | 48,0 | 38,6 | 28,0 | 25,3
N GEN 20; N2 flow [Nm3/h] | 7,5 | 6,6 | 30,2 | 24,6 | 20,9 | 17,3 | 11,5 | 5,7 | 3,5
Feed air consumption [Nm3/h] |  |  | 77,3 | 70,3 | 65,6 | 60,1 | 48,3 | 35,1 | 31,6
N GEN 25; N2 flow [Nm3/h] | 7,5 | 6,6 | 42,7 | 34,8 | 29,5 | 24,5 | 16,2 | 8,1 | 4,9
Feed air consumption [Nm3/h] |  |  | 109,4 | 99,4 | 92,8 | 85,0 | 68,4 | 49,6 | 44,7
N GEN 35; N2 flow [Nm3/h] | 7,5 | 6,6 | 67,4 | 55,0 | 46,6 | 38,6 | 25,6 | 12,8 | 7,9
Feed air consumption [Nm3/h] |  |  | 172,7 | 156,9 | 146,6 | 134,2 | 107,9 | 78,3 | 70,6
N GEN 60; N2 flow [Nm3/h] | 7,5 | 6,6 | 111,9 | 91,4 | 77,4 | 64,2 | 42,6 | 21,2 | 13,1
Feed air consumption [Nm3/h] |  |  | 286,9 | 260,6 | 243,5 | 223,0 | 179,3 | 130,1 | 117,3
N GEN 100; N2 flow [Nm3/h] | 7,5 | 6,6 | 192,9 | 157,5 | 133,5 | 110,6 | 73,4 | 36,6 | 22,5
Feed air consumption [Nm3/h] |  |  | 494,5 | 449,3 | 419,7 | 384,4 | 309,1 | 224,3 | 202,2
N GEN 200; N2 flow [Nm3/h] | 7,5 | 6,6 | 354,3 | 289,2 | 245,0 | 203,1 | 134,8 | 67,2 | 41,3
Feed air consumption [Nm3/h] |  |  | 907,9 | 824,8 | 770,6 | 705,8 | 567,5 | 411,8 | 371,3
N GEN 300; N2 flow [Nm3/h] | 7,5 | 6,6 | 590,9 | 482,4 | 408,7 | 338,8 | 224,8 | 112,0 | 68,9
Feed air consumption [Nm3/h] |  |  | 1514,3 | 1375,8 | 1285,3 | 1177,2 | 946,5 | 686,9 | 619,3
N GEN 400; N2 flow [Nm3/h] | 7,5 | 6,6 | 771,8 | 630,0 | 533,8 | 442,5 | 293,6 | 146,3 | 90,0
Feed air consumption [Nm3/h] |  |  | 1977,9 | 1797,0 | 1678,8 | 1537,6 | 1236,3 | 897,1 | 808,9
N-GEN SIZES

## Slide 21
CERTIFICATES
STANDARD
PED 2014/68/EU Pressure equipment directive (vessels are calculated for dynamic load)
2014/30/EU Electromagnetic compatibility
2014/35/EU Low voltage directive
OPTIONAL
ASME sec. VIII div.1
BV Marine, DNV, ABS, GL, …
ISO 13485
MDD

## Slide 22
CASE STUDY
CONTRACT SUPPLY
PSA
Nitrogen production 3.0 (99,9 %) | 
Investment value | 
Compressor KSA 22; 3,21m3/min, 10 bar | 
Refrigeration dryer OMD 175 | 
Pressure vessel TP500V13 | 
Pressure vessel TP300V | 
Filtration AF 0186 | 
Condensate drain ECD 40B | 
Activated carbon tower TAC 250 | 
Nitrogen generator N-GEN 50 | 
Total investment | 25.362 EUR
Simple depreciation at 8 years | 3.170 EUR
Variable costs | 
Energy costs - compressor KSA 22 | 220 kWh/day
Daily energy costs | 33 EUR/day
Annual service costs | 3.000 EUR
Total variable costs (energy+service)/year | 10 260 EUR
TOTAL ANNUAL COSTS | 13.430 EUR
Costs / 1 Nm3 | 0,13 EUR/Nm3
Annual costs | 13.000 EUR
Costs / 1 Nm3 | cca 0,4-0,7 EUR/Nm3
Annual nitrogen costs | 40.000 EUR

## Slide 23
CASE STUDY – GRAND KAFA
APPLICATION: TO PRESERVE AROMAS
AND SHELF LIFE OF THE COFFEE
NITROGEN PRODUCTION: 264 m3/h
PURITY: 99,9 %
COMPRESSED AIR
CONSUMPTION: 850 m3/h
Case study:
Grand Prom d.o.o.
Nitrogen production plant
Case study:
Grand Prom d.o.o.
Water cooling process

## Slide 24
OMEGA AIR d.o.o. Ljubljana
Cesta Dolomitskega odreda 10
SI-1000 Ljubljana, Slovenia
Tel.: +386 (0)1 200 68 00
Fax.: +386 (0)1 200 68 50
E-mail: info@omega-air.si
www.omega-air.si
THANK YOU FOR YOUR ATTENTION